## Slide 1
01 / OPENING
The building is now a machine
MECH × EEE
01 / 10
Future of Smart Buildings · BMS · IoT · AI · Energy Management
Buildings eat 30% of the world’s energy. Most of them still run on guesswork.
▸ IEA: buildings take ~30% of global final energy and ~26% of energy-related CO2.
▸ UNEP: buildings & construction ~37% of energy-related CO2 — retrofit decides the next 20 years.
▸ Most commercial HVAC still sequences on clocks and design loads, not occupancy, weather, or tariff.
▸ The bottleneck is integration and control logic — not another chiller brand.
▸ Mech owns the physics; EEE owns the electrons. Software without that literacy fails in the plant room.
Visual: night tower + ducts/busbars. One huge 30%.
HOLD THIS
30%
of global final energy in buildings (IEA)
Notes: Open with the 10-second hook, then land 30% on screen. Pause after “guesswork.” This hour is a map of where Mechanical and EEE work sits in a smart building — not a vendor tour.

## Slide 2
02 / DEFINITION
What “smart” actually means
MECH × EEE
02 / 10
Future of Smart Buildings · BMS · IoT · AI · Energy Management
A smart building is a closed-loop control system with a carbon and rupee constraint.
▸ Sense: T, RH, CO2, occupancy, kW/kWh, flow, pressure, lux, equipment status.
▸ Decide: BMS sequences and setpoints — ASHRAE logic before apps.
▸ Actuate: valves, dampers, VFDs, lighting, ATS/DG, chillers, pumps.
▸ Verify: submetering and trends. If you cannot prove 12%, you did not save 12%.
▸ Example: occupancy + CO2 resets outdoor air; tariff sheds non-critical loads.
Visual: four-layer stack with Mech vs EEE ownership tags.
HOLD THIS
S→D→A→V
Sense · Decide Actuate · Verify
Notes: Draw the loop if you can. Ask: where does your final-year project sit — sensor, controller, or actuator?

## Slide 3
03 / BMS
The building’s operating system
MECH × EEE
03 / 10
Future of Smart Buildings · BMS · IoT · AI · Energy Management
If the BMS is weak, IoT and AI are decoration on a broken plant.
▸ A BMS is a distributed control system: controllers, I/O, workstation, trends, alarms — cousin to DCS/SCADA.
▸ Sequences (ASHRAE Guideline 36 trim-and-respond) can cut fan energy 10–30% vs fixed setpoint.
▸ Mid-size office: often 2,000–8,000 points. Naming and calibration decide maintainability.
▸ Meters, DG, UPS, lifts, lighting on one time-synced historian.
▸ Commissioning / retro-commissioning often finds 5–20% before any AI purchase.
Visual: chiller → pumps → AHUs → VAV with BACnet objects.
HOLD THIS
5–20%
typical savings from commissioning alone
Notes: BMS work is control engineering, not clicking graphics. 24×7 IT campuses: latent load and unreliable grid make sequences and backup power the same design.

## Slide 4
04 / IOT
From sparse sensors to a dense twin
MECH × EEE
04 / 10
Future of Smart Buildings · BMS · IoT · AI · Energy Management
IoT does not replace the BMS. It densifies the measurement layer it always needed.
▸ Classic BMS: a few zone sensors. IoT: occupancy, IAQ, plug meters, vibration — often 5–10× more points.
▸ Wireless (LoRaWAN, BLE, Wi-Fi, NB-IoT) instruments existing campuses without tearing every ceiling.
▸ Occupancy-driven HVAC commonly shows 10–25% HVAC reduction when schedules match reality.
▸ EEE: CT/PT accuracy and OT security. A 2% CT error wrecks a 5% “AI savings” claim.
▸ Mech: sensor placement, stratification, dirty filters that make a dashboard lie.
Visual: occupancy heatmap vs a dirty, uncalibrated duct sensor.
HOLD THIS
10–25%
HVAC energy when schedules match occupancy
Notes: IoT without calibration is noise. Story: a CO2 sensor in return air that “proved” a packed exam hall was empty.

## Slide 5
05 / AI
From rules to prediction
MECH × EEE
05 / 10
Future of Smart Buildings · BMS · IoT · AI · Energy Management
Use AI to find the broken valve and tomorrow’s peak — not to reinvent thermodynamics.
▸ Fault detection (FDD): stuck dampers, simultaneous heat/cool, fouled condensers — 10–30% avoidable waste.
▸ Load and occupancy forecasting for chiller staging, storage, and DG/grid decisions.
▸ Supervisory optimization proposes setpoints; BMS still executes interlocks, freeze protection, fire modes.
▸ Data-centre ML cooling is a cousin idea — occupied buildings are messier. Transfer the method, not the hype.
▸ Guardrail: a model that “saves energy” by starving outdoor air is a health failure.
Visual: FDD fault tree | 24-hour kW forecast vs demand-limit band.
HOLD THIS
AI ⊂ BMS
supervisor, not the safety layer
Notes: Say slowly: AI is a supervisor, BMS is the operator, physics is the law. Example: detecting a 3°C chilled-water delta-T collapse before the bill arrives.

## Slide 6
06 / ENERGY
The scoreboard and the market
MECH × EEE
06 / 10
Future of Smart Buildings · BMS · IoT · AI · Energy Management
Energy management is not a green poster. It is metered, tariff-aware, plant-level control.
▸ Split meters: incoming HT/LT, chiller plant, lighting, plug, critical IT — or “8% savings” is a story.
▸ India: ToD tariffs, demand charges, DG at ~₹25–40/kWh. Shaving 100 kW at 18:00 can beat a 5% all-day kWh cut.
▸ Thermal storage, pre-cooling, and kW/TR are Mechanical core — now visible in real time.
▸ Solar + BMS interlocks so PV does not fight the diesel plant (EEE: inverters, harmonics, islanding).
▸ A plant at 0.55–0.70 kW/TR vs neglected 0.90–1.1 kW/TR is a larger lever than swapping every LED twice.
Visual: Sankey — grid + DG + solar → chillers, AHUs, lighting, IT.
HOLD THIS
kW/TR
the plant KPI that beats a green poster
Notes: Put simple bill math on screen: demand vs energy charge. Tie it to VFDs, staging, and power factor.

## Slide 7
07 / STACK
One building, four layers
MECH × EEE
07 / 10
Future of Smart Buildings · BMS · IoT · AI · Energy Management
The future building is not four products. It is one control and data architecture.
▸ Working stack: calibrated sensors, documented sequences, open protocols, historian, KPIs operators actually open.
▸ Typical stack: ~10% from sequences, 5–15% from sensors/ops, plus peak cuts.
▸ Digital twins are useful when anchored to live points and physics — not pretty BIM with fake occupancy.
▸ Unsegmented BACnet on the corporate LAN is a design defect. OT/IT zoning belongs in EEE for buildings too.
▸ Operators override “because 4th floor is always hot.” Fix the floor, or the AI is dead by Friday.
Visual: field → controllers → BMS/historian → analytics, with a security band across OT.
HOLD THIS
OT ≠ IT
segment the network or inherit the incident
Notes: Systems-thinking slide. Point at Mech and EEE: who owns cybersecurity? Both, plus IT.

## Slide 8
08 / CAREERS
Where Mech and EEE actually work
MECH × EEE
08 / 10
Future of Smart Buildings · BMS · IoT · AI · Energy Management
The scarce graduate is not “someone who heard of IoT.” It is someone who can commission a plant.
▸ Mechanical: HVAC design, energy models, retro-commissioning, IAQ, fire-smoke control interfaces.
▸ EEE: ELV/BMS, SCADA, metering, VFD harmonics, protection, microgrids, EV charging load.
▸ Shared: controls engineer, energy manager, commissioning authority, campus ESG data owner.
▸ India demand: GCCs, hospitals, airports, data centres, manufacturing parks — plant + digital, not smart-city slogans.
▸ Hire-ready project: BACnet/Modbus logger + chiller kW/TR dashboard + a documented sequence.
Visual: two-column job map; overlap = Controls & Energy.
HOLD THIS
Cx
commissioning is the bilingual skill
Notes: Internships: FM, controls OEMs, ESCOs, data-centre MEP. Portfolio = points list + sequence + trend, not only CAD.

## Slide 9
09 / LIMITS
What can go wrong
MECH × EEE
09 / 10
Future of Smart Buildings · BMS · IoT · AI · Energy Management
A building that saves energy by making people sick is not sustainable. It is a failed controller.
▸ Comfort, IAQ, and safety override energy KPIs — always. OA cutbacks without CO2/PM are a health failure.
▸ A ₹2 crore analytics overlay on failed valves is malpractice. 5–20% often sits in maintenance.
▸ Proprietary protocols and cloud-only historians create stranded assets.
▸ Rebound: report absolute kWh and intensity (kWh/m², kWh/occupant), not only % vs last year.
▸ Match compute to the plant. Edge FDD is cheap; giant remote models on a 200 TR plant can be theatre.
Visual: risk matrix — IAQ, cyber, lock-in, payback, data quality.
HOLD THIS
IAQ > kWh
energy never outranks health or fire mode
Notes: This slide earns trust. Do not rush. You will use it when someone says AI is hype or smart buildings are only for rich campuses.

## Slide 10
10 / CLOSE
Make this one tell the truth
MECH × EEE
10 / 10
Future of Smart Buildings · BMS · IoT · AI · Energy Management
Don’t wait for a smarter building. Learn to make this one tell the truth.
▸ Truth = calibrated sensors + documented sequences + submetering + an operator allowed to act.
▸ CTA: pick one AHU or one incoming feeder. Trend it 14 days. Bring waste in kWh, kW, or °C — not slogans.
▸ A commissioning walk-through teaches more than a week of smart-city videos.
▸ Build bilingual skill: one plant diagram + one electrical single-line + a points list.
▸ The industry does not need more people who can say “digital twin.” It needs people who can explain 1.0 kW/TR.
Visual: dark slide, one sentence, one CTA. No collage.
HOLD THIS
14 days
one real loop, then you have evidence
Notes: Deliver the close standing still. End on the CTA, then the thank-you. Leave 8–10 minutes for hard questions. Thank them as future operators of India’s next 20 years of floor space.